## Slide 1: Water Pollution in Japan
16 March 2011
JEMAI
Kenzo OOKA

## Slide 2: History of regulated pollutants
1971: Eight substances including cadmium were regulated
1975: PCB added
1989: TCE and PCE
Underground water was regulated under Water Control Law
1993: 13 VOCs
2001: Boron and Fluorine (Hoso & fusso ), Nitrogen compounds etc.
2010: Four chemicals were newly added to the water standards etc.
1,4-Dioxane,
Vinyl Chloride (Chloroethylene or enbimonoma),
1,2-Dichloroethylene (cis plus trans),
1,1-Dichloroethene
(1,4-ジオキサン、塩化ビニルモノマー、1,2-ジクロロエチレン、1,1-ジクロロエチレン)

## Slide 3: Water quality Standards in Japan
Since 1971 surface water has been inspected by local government in Japan for 8 substances such as cadmium and total cyanide etc. (human health items).
Now we have 26 substances for monitoring by government.
Each standard is applied for any public water bodies such as rivers, lakes, and sea (especially bays), however, fluorine and boron are not applied for seawater.
Almost all water samples (>99%) are within the standards in FY2007 http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf
Please see the graph and consider following questions:
Why arsenic and lead are increased?
Do they consider natural contamination levels?

## Slide 4: Samples exceeding water environmental standards in Japan (%) FY1971 - FY2007
Cadmium
Total Cyanide
Lead
Chrome 6
Arsenic
Total mercury
PCB
1993
http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf

## Slide 5: Annual average BOD and COD analysis
90.0% of rivers, 50.3% lakes, and 78.7% seawater satisfy the standards in 2007
Arsenic : from 0.05mg/L to 0.01mg/L (1993)
Lead: from 0.1mg/L to 0 .01mg/L (1993)
River BOD
Lake COD
Sea COD
http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf

## Slide 6: Groundwater contamination
Samples of 325 wells (7.0%) out of 4,631 wells are exceeding the groundwater standards in FY2007.
Among regularly monitoring wells (4,854) there are 1,999 contaminations exceeding the standards.
VOCs are one of the major pollutants in Japan.
T-N problems are derived from agriculture etc.
(livestock, manure/fertilizer, and sewage etc.)
http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf

## Slide 7: Samples exceeding groundwater standards in Japan (%) FY1971 - FY2007
Nitrogen
Arsenic
Fluorine
Tetrachloroethylene
Trichloroethylene
Lead
Arsenic : from 0.05mg/L to 0.01mg/L and Lead: from 0.1mg/L to 0 .01mg/L (1993)
1993
http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf

## Slide 8: Water Pollution Incidents 1989 - 2007
Number of Pollution Incidents
related to major rivers in Japan
http://www.env.go.jp/water/confs/fpwq/01/mat03_1.pdf

## Slide 9: What has happened in Japan?
Amendments for the Water Pollution Prevention Act in 2011,
Which will be enacted 1 April 2012.
  In case of pollution incidents (discharge) the premises managers will be legally required to do countermeasures and reporting to the authorities.
  Causes of discharge will include gradual pollution such as ‘become too old and following leakage’ , natural disasters, heavy rain or flood, fire & explosion.
  Newly selected 58 Pollutants such as Cu, Zn, Fe, Toluene, NaOH(sodium hydroxide), NaClO (sodium hypochlorite)etc.

## Slide 10: Telemeter System
Waste Incinerator 24 hours
Continuous Emission
Monitoring System (CEMs)
􀂾 SOX conc. (1ppm)
􀂾 NOX conc. (46ppm)
􀂾 Hcl conc. (4ppm)
􀂾 CO conc. (0.0%)
􀂾 O2 conc. (6.8%)
􀂾 Temp (1319℃)
In case of Boiler
Fuel consumption ( kl/h ) etc.
http://www.pref.kagawa.jp/teshima/internet/
Local Government Office
Checks Emission Compliance
for 24 hours 365 days a year
Data Sending Device